# Build U-Boot and Linux Kernel from Source Code

The source code of U-Boot boot loader and Linux kernel can be fetch from the Git server(Toradex Repository):
git clone -b <git-branch> git://git.toradex.com/u-boot-toradex.git
git clone -b <git-branch> git://git.toradex.com/linux-toradex.git

Ex.
git clone -b 2015.04-toradex git://git.toradex.com/u-boot-toradex.git
git clone -b toradex_vf_4.1 git://git.toradex.com/linux-toradex.git

Vybrid U-Boot Versions
Image Version	: V2.4 / V2.5
U-Boot Git Branch	: 2015.04-toradex
U-Boot Configuration	: colibri_vf_defconfig
U-Boot Binary	: u-boot-nand.imx

Vybrid Linux Kernel Versions
Image Version	: V2.5
Kernel git branch	: toradex_vf_4.1
Kernel Configuration	: colibri_vf_defconfig
Device Tree	: vf500-colibri-eval-v3.dtb
Kernel Binary	: arch/arm/boot/zImage

# U-Boot
Configuration
Make colibri_vf_defconfig
Compilation
make -j3 2>&1 | tee build.log
Update
Replace the existing u-boot.imx to new compiled u-boot.imx.
Boot the module to the U-Boot prompt and update U-Boot:
run setupdate
run update_uboot

To reset the environment to the updated default environment, enter the following from the command line of the updated U-Boot:
env default -a
saveenv

# Linux Kernel
Kernel Configuration
 make colibri_vf_defconfig
make menuconfig
Kernel Compilation
make -j3 zImage | tee build.log
make vf500-colibri-eval-v3.dtb
Kernel Update
cd ~/Colibri_VF_LinuxImageV2.3/rootfs/boot
cp ~/linux-toradex/arch/arm/boot/zImage ./zImage-custom
cp ~/linux-toradex/arch/arm/boot/dts/vf500-colibri-eval-v3.dtb ./vf500-custom.dtb
ln -fs /boot/zImage-custom zImage
ln -fs /boot/vf500-custom.dtb vf500-colibri-eval-v3.dtb
cd ../..

Boot the module to the U-Boot prompt and update the whole root file system which contains the new kernel in its /boot folder:
run setupdate
run update_rootfs