# Flashing Embedded Linux to Vybrid Modules

Vybrid have the following flashing methods are currently possible:
- Using an SD card
- Using a USB flash drive aka memory stick
- Using TFTP over Ethernet

Flash Using an SD card : Use the flashing utilities provided by the Toradex image
- Use any VFAT formatted SD/uSD card or USB flash drive with at least 1000 MB of free space
- Optionally: Format the SD/uSD card using the format_sd.sh script
  - ./format_sd.sh -d /dev/mmcblk0
  - Ex. ./format_sd.sh -d /dev/sdc
- Run the update.sh script with the -o argument pointing to the mount point of the SD card or USB flash drive. For example assuming the SD card is mounted at /media/sdcard
  - ./update.sh -o /media/sdcard/
At this point the SD card or USB flash drive should contain U-Boot, flash scripts and the UBI root file system image.
Note: U-Boot expects a partition table (MBR) on the SD card or USB flash drive.
## Flashing from U-Boot
Insert the prepared media into carrier board
  - SD card into SD card/MMC SDIO-socket (X15 on Evaluation Board, X10 on Iris)
  - USB flash drive using a standard USB host plug (e.g. X31/X32 on Evalution Board, X11 on Iris, top X6 on Viola)
- Connect the serial console to your host PC
    - Evaluation Board V3.1a/V3.2a: 115200 baud on UART_A (lower X25 resp. X27 depending on JP17/19) without any handshake
    - Iris V1.1a: 115200 baud on UART_A (X13) without any handshake
- Apply power or reset
- Hit any key immediately to stop auto booting

At this point the U-Boot prompt should be visible.
Use 'run setupdate' and 'run update' command to update the module
Colibri VFxx # run setupdate
Colibri VFxx # run update

If in case mmc not detect then rescan using below command:
Colibri VFxx # mmc rescan; fatload mmc 0:1 ${loadaddr} flash_mmc.img; source ${loadaddr}

## Flashing from Scratch
Colibri VFxx # nand erase.chip
Colibri VFxx # run setupdate
Colibri VFxx # run create_bcb
Colibri VFxx # cfgblock create
Is the module an IT version? [y/N] y
Enter the module version (e.g. V1.1B): V1.1B
Enter module serial number: 04815386
Toradex config block successfully written
Colibri VFxx # run update
## Connecting serial port
The Colibri VFxx modules support serial recovery only using UART_A. Serial recovery requires hardware flow control with RTS/CTS signals. As the boot ROM is able to keep up with the incoming data the flow control signals can simply be bridged if required. However we recommend to use RTS/CTS whenever possible. When starting the serial downloader utility remember whether you have RTS/CTS connected or bridged.

# VFxx Recovery Mode
- In case your module doesn't boot at all, you can download the boot loader directly into the modules memory using the serial port UART_A
### Iris Carrier Board 1.1A
  - Short the pad 1 and 2 of JP1 in Iris using a wire.
  - Power up Iris board.
  - Remove the wire.
Linux
On Linux, the utility imx_uart is called by our update shell script:
./update.sh -d /dev/ttyUSB0
In case RTS/CTS are not connected, use the parameter -n:
./update.sh -n -d /dev/ttyUSB0

However since the boot loader did not work anymore it is likely that there is something wrong with the initial boot configuration block (BCB). To recreate the BCB use the below mention commands.
Colibri VFxx # run setupdate
Colibri VFxx # run create_bcb
Colibri VFxx # cfgblock create
Is the module an IT version? [y/N] y
Enter the module version (e.g. V1.1B): V1.1B
Enter module serial number: 04815386
Toradex config block successfully written

Flash Using TFTP over Ethernet
### Kernel from TFTP and Rootfs from NFS
  - Install and configure a DHCP, TFTP and NFS server on your development workstation
    - U-Boot obtains the IP address and the name of the file containing the kernel from the DHCP server.
    - U-Boot loads the kernel from the TFTP server with 'serverip' address.
    - U-Boot sets the kernel's commandline so that the kernel mounts the rootfs from a NFS server.
    - Linux uses DHCP again to get an IP address and the root-path arguments.
    - Linux tries to mount the NFS root file system using the root-path.

## Prepare Kernel and rootfs
    - TFTP
        Copy the kernel and if applicable the device-tree to the tftp directory. Make sure that the kernel file name matches with the filename field you specified in the DHCP configuration and the device tree name with the name configured in U-Boot.
    - sudo cp -Ppr /path to kernel/uImage* /srv/tftp/

NFS
Copy the rootfs to /srv/nfs/rootfs (while preserving symlinks, timestamps..)
sudo cp -Ppr /path to image/rootfs/* /srv/nfs/rootfs

#### Restart the Servers : Ubuntu: mk@ubuntu: ~ $ sudo service isc-dhcp-server restart; sudo service tftpd-hpa restart; sudo service nfs-kernel-server restart

#### U-Boot Variables for TFTP/NFS Boot
Ex.
ipaddr=192.168.10.2
serverip=192.168.10.1
ethaddr=00:14:2d:48:8a:58
The nfsrootdebug cmdline option enables debugging messages to debug mounting root file system via NFS:
defargs=$defargs nfsrootdebug

#### Booting
stop in U-Boot and then:
run nfsboot
to make this the default boot option:
setenv bootcmd 'run nfsboot'
saveenv

SD BOOT
1. Prepare Sd card for the Sd booting:
  ./format_sd.sh -f -d /dev/xxx (ex./dev/mmcblk0 or /dev/sdc)
  "-f" option will additionally copy the rootfs into the second partition.
2. From uboot, one can then boot from the SD card by executing "run sdboot" command or if you want to make it everytime booting from the sdcard then update the environment variable bootcmd and set "run sdboot" first.see the example below:
  setenv bootcmd "run sdboot ; run ubiboot; run nfsboot"
  saveenv
  reboot