# Creating and flashing UBI / UBIFS images.

JFFS2 has been widely used but has several performance issues

### Why flash-oriented filesystems ?
- MTDs (Memory Technology Devices) are very different from block devices: instead of a sequence of writable sectors, they contain an array of writable pages, organized in so-called “erase blocks”.
- To write on a page that already has data on it, you first have to erase this data. However, it is only possible to erase whole eraseblocks. Only then, you can write your new data (including what you didn’t change). Erasing causes the memory cells to wear out. At some point, they won’t be usable anymore and have to be skipped.
- it is memory-based, random access is theoretically as fast as sequential access. So, you don’t need to keep the fragments of your files together. It makes it possible to do wear-leveling and thus, “increase” the lifetime of the chip.
- A simple way of doing wear-leveling is to keep track of the number of times a block has been erased and use the block that has been the least erased when updating data.
- All these constraints make it hard to write a flash filesystem.
- UBI intends to deal with all MTD-specific operations while still presenting random-access volumes to the the upper-layer. The first – and as for now, only – implementation using UBI is UBIFS. UBI is a “volume manager” and maps physical erase blocks (PEB) to logical erase blocks (LEB). The LEBs are smaller than the PEBs because of meta-data and headers.
### How to use UBI Filesystem on my board?
- There are mainly 2 ways to do that:
### Solution A – On a booted Linux system
### Solution B – Prepare a UBI image ready to be flashed
- Whatever solution you choose, you need to know the sizes of:
  - The eraseblocks (PEB)
  - The pages (or “minimum input/output size”)
  - The subpages (it may be the same as the min i/o size)
- you can deduce another one: the size of logical erase blocks. It is the size of the PEB minus a data offset which is:
  (int((Subpage_size + Page_size) / Page_size)) * Page_size
  - This formula makes some assumption but should be correct if the subpage size is more than 8B and the page size more than 64B.
  - The best way to be sure of this size is to use mtdinfo on linux on the board. mtdinfo is part of the ubi-utils (part of mtd-utils). It’s probably available in your build system.
- For creation of ubifs filesystem, we used mtd-utils and it provides command mkfs.ubifs.
  # mkfs.ubifs -r </path/to/your/rootfs/tree> -m <min io size>
  -e <LEB size> -c <Eraseblocks count>
  -o </path/to/output/ubifs.img>
### Solution A – On a booted Linux system
- You first need to enable UBI and UBIFS in the kernel and install the mtd-utils package on your box. You may also compile mtd-utils from its sources.
- Once you have your UBIFS image at hand, follow below steps:
  # ubiformat /dev/mtdX
  # ubiattach -p /dev/mtdX
  # ubimkvol /dev/ubi0 -N volume_name -s 64MiB
  # ubiupdatevol /dev/ubi0_0 /path/to/ubifs.img
  # mount -t ubifs ubi0:volume_name /mount/point
- ubiformat erases an MTD partition but keeps its erase counters
- ubiattach creates a UBI device from the MTD partition. This UBI device is then referred to by UBI as ubi0
- ubimkvol creates a volume on a UBI device ; this volume is referred to as ubi0_0
- ubiupdatevol puts an image on an empty volume.
- At last, the well-known mount can be invoked using <device>:<volume>
#### Solution B – Prepare a UBI image ready to be flashed
- It is more common to directly flash filesystem images directly from the bootloader.
- It is made possible by ubinize to prepare a UBI device image containing one or more volumes.
- ubinize reads a configuration file (in the very simple INI format) describing the volumes and their configuration.
- Example :
  - two volumes ; one, named rootfs is read-only (static), the other one, data is read-write (dynamic)
  - the autoresize flag makes UBI resize to volume to use the whole unused space at initialization.
    Static Example:
[rootfs_volume]
mode=ubi
image=rootfs.ubifs
vol_id=1
vol_type=static
vol_name=rootfs
vol_alignment=1
Dynamic Example:
[rwdata-volume]
mode=ubi
image=data.ubifs
vol_id=2
vol_type=dynamic
vol_name=data
vol_alignment=1
vol_flags=autoresize
- Next is the generation of the UBI image. The ubinize utility will need the Physical Erase Block size (PEB) (option -p) and the minimum I/O size (-m):
  - # ubinize -vv -o <output image> -m <min io size>
  -p <PEB size>KiB <configuration file>
### Use a UBIFS partition as root partition
Some options need to be passed to the kernel to boot on a ubi volume and on a UBIFS partition:
ubi.mtd=<mtd partition number>
root=<ubi device>:<volume>
rootfstype=ubifs
For Example : ubi.mtd=1 root=ubi0:rootfs rootfstype=ubifs

In our case we used this:
mkfs.ubifs --space-fixup -c 8112 -e 124KiB -m 2KiB -o ubifs.img -r rootfs/ -v
Parameters:
-c <Eraseblocks count>
-e <LEB size>
-m <min io size>
-o </path/to/output/ubifs.img>