# Setting up the Eclipse IDE for Yocto Application Development

Requirements
1) Linux machine. Ubuntu 12.4 or higher is recommended.
2) Yocto BSP (It is board specific)
3) Poky Meta Toolchain
For information on how to extract and install the meta toolchain please follow the steps on the next document.
$ bitbake meta-toolchain
4) Eclipse Setting:

Setting Up the Eclipse IDE
To develop within the Eclipse IDE, you need to do the following:
1. Install the optimal version of the Eclipse IDE.
2. Configure the Eclipse IDE.
3. Install the Eclipse Yocto Plug-in.
4. Configure the Eclipse Yocto Plug-in.
##### Installing the Eclipse IDE
- It is recommended that you have the Luna SR2 (4.4.2) version of the Eclipse IDE installed on your development system.
- If you do not have the Luna SR2 (4.4.2) Eclipse IDE installed, you can find the tarball at http://www.eclipse.org/downloads. From that site, choose the appropriate download from the "Eclipse IDE for C/C++ Developers". This version contains the Eclipse Platform, the Java Development Tools (JDT), and the Plug-in Development Environment.
  - $ cd ~
     $ tar -xzvf ~/Downloads/eclipse-cpp-luna-SR2-linux-gtk-x86_64.tar.gz
##### Configuring the Eclipse IDE
##### This section presents the steps needed to configure the Eclipse IDE
Before installing and configuring the Eclipse Yocto Plug-in, you need to configure the Eclipse IDE. Follow these general steps:
1. Start the Eclipse IDE.
2. Make sure you are in your Workbench and select "Install New Software" from the "Help" pull-down menu.
3. Select Luna - http://download.eclipse.org/releases/luna from the "Work with:" pull-down menu. [luna/kepler/mars]
4. Expand the box next to "Linux Tools" and select the Linux Tools LTTng Tracer Control, Linux Tools LTTng Userspace Analysis, and LTTng Kernel Analysis boxes. If these selections do not appear in the list, that means the items are already installed.
5. Expand the box next to "Mobile and Device Development" and select the following boxes. Again, if any of the following items are not available for selection, that means the items are already installed:
- C/C++ Remote Launch (Requires RSE Remote System Explorer)
- Remote System Explorer End-user Runtime
- Remote System Explorer User Actions
- Target Management Terminal (Core SDK)
- TCF Remote System Explorer add-in
- TCF Target Explorer
1. Expand the box next to "Programming Languages" and select the C/C++ Autotools Support and C/C++ Development Tools boxes. For Luna, these items do not appear on the list as they are already installed.
2. Complete the installation and restart the Eclipse IDE.

##### Installing or Accessing the Eclipse Yocto Plug-in
To install the Eclipse Yocto Plug-in from the update site, follow these steps:
Start up the Eclipse IDE.
In Eclipse, select "Install New Software" from the "Help" menu.
Click "Add..." in the "Work with:" area.
Enter http://downloads.yoctoproject.org/releases/eclipse-plugin/1.8/luna in the URL field and provide a meaningful name in the "Name" field.
Click "OK" to have the entry added to the "Work with:" drop-down list.
Select the entry for the plug-in from the "Work with:" drop-down list.
Check the boxes next to Yocto Project ADT Plug-in, Yocto Project Bitbake Commander Plug-in, and Yocto Project Documentation plug-in.
Complete the remaining software installation steps and then restart the Eclipse IDE to finish the installation of the plug-in.
##### Configuring the Eclipse Yocto Plug-in
Configuring the Eclipse Yocto Plug-in involves setting the Cross Compiler options and the Target options. The configurations you choose become the default settings for all projects. You do have opportunities to change them later when you configure the project (see the following section).
To start, you need to do the following from within the Eclipse IDE:
- Choose "Preferences" from the "Window" menu to display the Preferences Dialog.
- Click "Yocto Project ADT" to display the configuration screen.

###### Configuring the Cross-Compiler Options
To configure the Cross Compiler Options, you must select the type of toolchain, point to the toolchain, specify the sysroot location, and select the target architecture.
- Selecting the Toolchain Type: Choose between Standalone pre-built toolchain and Build system derived toolchain for Cross Compiler Options.
  - Standalone Pre-built Toolchain: Select this mode when you are using a stand-alone cross-toolchain. For example, suppose you are an application developer and do not need to build a target image. Instead, you just want to use an architecture-specific toolchain on an existing kernel and target root filesystem.
  - Build System Derived Toolchain: Select this mode if the cross-toolchain has been installed and built as part of the Build Directory. When you select Build system derived toolchain, you are using the toolchain bundled inside the Build Directory.
- Point to the Toolchain: If you are using a stand-alone pre-built toolchain, you should be pointing to where it is installed. If you used the ADT Installer script and accepted the default installation directory, the toolchain will be installed in the /opt/poky/1.8 directory. Sections "Configuring and Running the ADT Installer Script" and "Using a Cross-Toolchain Tarball" in the Yocto Project Application Developer's Guide describe how to install a stand-alone cross-toolchain.
  If you are using a system-derived toolchain, the path you provide for the Toolchain Root Location field is the Build Directory. See the "Using BitBake and the Build Directory" section in the Yocto Project Application Developer's Guide for information on how to install the toolchain into the Build Directory.
- Specify the Sysroot Location: This location is where the root filesystem for the target hardware resides. If you used the ADT Installer script and accepted the default installation directory, then the location in your home directory in a folder named test-yocto/target_arch. Additionally, when you use the ADT Installer script, the /opt/poky/1.8/sysroots location is used for the QEMU user-space tools and the NFS boot process.
  If you used either of the other two methods to install the toolchain or did not accept the ADT Installer script's default installation directory, then the location of the sysroot filesystem depends on where you separately extracted and installed the filesystem.
  For information on how to install the toolchain and on how to extract and install the sysroot filesystem, see the "Installing the ADT and Toolchains" section in the Yocto Project Application Developer's Guide.
- Select the Target Architecture: The target architecture is the type of hardware you are going to use or emulate. Use the pull-down Target Architecture menu to make your selection. The pull-down menu should have the supported architectures. If the architecture you need is not listed in the menu, you will need to build the image. See the "Building an Image" section of the Yocto Project Quick Start for more information.

###### Configuring the Target Options
You can choose to emulate hardware using the QEMU emulator, or you can choose to run your image on actual hardware.
- QEMU: Select this option if you will be using the QEMU emulator. If you are using the emulator, you also need to locate the kernel and specify any custom options.
  If you selected Build system derived toolchain, the target kernel you built will be located in the Build Directory in tmp/deploy/images/machine directory. If you selected Standalone pre-built toolchain, the pre-built image you downloaded is located in the directory you specified when you downloaded the image.
  Most custom options are for advanced QEMU users to further customize their QEMU instance. These options are specified between paired angled brackets. Some options must be specified outside the brackets. In particular, the options serial, nographic, and kvm must all be outside the brackets. Use the man qemu command to get help on all the options and their use. The following is an example:
  serial ‘<-m 256 -full-screen>’
  Regardless of the mode, Sysroot is already defined as part of the Cross-Compiler Options configuration in the Sysroot Location: field.
- External HW: Select this option if you will be using actual hardware.

HOW TO EXTRACT SDK FOR YOCTO ECLIPSE PLUGIN?

- Got to sdk path then
  - sh script_name.sh
    - Provide path for SDK extract
- Then, go to eclipse windos->preferences->Yocto Project ADT
  - Cross-compiler option
    - Standalone *
    - Toolchain root location: Provide path for toolchain.
      - Ex. /eclipse_sdk/oe_sdk/
    - Sysroot Location: Provide sysroot path
      - Ex. /eclipse_sdk/oe_sdk/sysroots
  - Target Option
    - Qemu
    - External H/W